## Slide 1: CUDA SPICE Circuit Simulator
Milestone 1
Angelina Risi, EE 2018

## Slide 2: What is SPICE?
Simulation Program with Integrated Circuit Emphasis
Basis of most modern simulators (ngspice, Cadence (PSpice), etc)
First version in 1973
Has fairly well-documented netlist/input file format

## Slide 4: Milestone 1 Features
Partial file parsing – only reads Resistors, VDC, IDC, VCCS elements from input SPICE netlists
DC Operating Point simulation for simple, (ideally) fully linear circuits
  Started with CPU implementation
  Moved matrix solving code to GPU
Began adding code for transistor (nonlinear) implementation
  Element structure, current calculation
  Currently working on framework for non-linear convergence

## Slide 5: Linear Solver
Circuit elements are converted into Conductance, Current, and Voltage matrices, initialized at 0.0f
Kirchhoff’s Current Law and Ohm’s Law
[ G ] * [ V ] = [ I ], solve for V
  Matrix reduction
  Plug in known voltages (e.g. voltage source with one end to GND)
  Solve

## Slide 7: Plans for NON-Linear Convergence
SPICE apparently uses Newton-Raphson Method
  Successive approximation until error within tolerance
Start with “guess” voltages for unknown non-linear dependencies
  Substitute into equations to populate matrices
Linear solver for new voltage estimate
  If outside of tolerance, new guess and try again
Parallelization ideas:
  Guess voltage and current calculations in parallel for each node
  First guess multiple values in parallel and choose nearest?

## Slide 8: IMPROVEMENTS NEEDED Next MILESTONE
Complete netlist and model file parsing
DC Sweep simulation
Full 1st order transistor implementation (which means ignoring 2nd order effects, e.g. body, channel length modulation)
  Working non-linear solver
Branch current calculation