## Slide 1: CUDA SPICE Circuit Simulator
Milestone 2
Angelina Risi, EE 2018

## Slide 2: Progress Since Milestone 1: Transistors
Added transistor parsing, not including any extra geometry/layout parameters
Currently use a default hard-coded NMOS model, need to add model parsing
Transistor linearization to G and I elements
Solution of circuits including transistors by:
  Using previous solution as “Guess” voltages to linearize model
  Iterating solving circuit until new solution and previous guess converge to within some absolute tolerance (currently 1µV)
  This implicitly performs Newton-Raphson method
  Currently very serial method, only matrix solving on GPU

## Slide 4: Progress Since Milestone 1:
Code cleanup: overhaul on how we handle circuit elements
  Instead of separate structs and lists for each type of element, all passives are the same Element with node and parameter arrays (instead of hardcoding how many they have)
    Other than voltage sources, all passives can be stored on the same list (because VDC needs to be applied last to matrices for reasons described below
More edge case testing to locate and correct bugs
  Located a problem with VDC modelling (problem with conversion to I and G when neither node grounded)
    Before: Used the fact that the currents flowing out of both positive and negative node are equal to generate G and I matrix entries
    Problem: Even though Vp = Vn + Vdc used to replace on of the voltages in one of the equations to assert Vdc dependence, still dependent on G seen at each node
    Solution: seems really obvious, but Vp – Vn = Vdc, => Vp(Gx) – Vn(Gx) = Vdc(Gx) => set Gx = 1. We still use the equal currents to generate the Vn row of the matrix, but the Vp row is replaced with 1 in Vp column and -1 in Vn column and Vdc in I va

## Slide 6: Currently Working ON:
Model parsing and multiline content parsing
  Models generally specified in separate .incude files, but can be in netlist file, .model line
  Parameters spilling into multiple lines start new line with ‘+’ character, need to look ahead to next line
DC Sweep – already have idea of how to setup
  Find swept element, save original parameter value, overwrite with start value
  Solve, increment value by step size, repeat until stop value reached
Porting matrix setup to GPU:
  Parallelize by elements
  Atomics for race conditions between elements on same node

## Slide 7: Next MilestonE:
Transient (Time step) Simulation
  Add in capacitors, inductors, AC sources (time-dependent elements)
Second-order effects (improved transistor modelling)
Graphical interface or data export and plotting
Performance optimizations & comparison
Stream compaction of matrices (expected to be sparse in large circuits)